## Slide 1
EQ2341 Assignment 5
System Demonstration: Song Recognition
Hanqi Yang, hanqi@kth.se
Qian Zhou, qianzho@kth.se
May 27th, 2022
Notes: Remember to introduce our country, major.

## Slide 2
Application and Database
  Distinguishing between a few brief snippets of hummed melodies.
  We use our own data and voices to train.
 |  | Training |  | Test | 
 |  | Hanqi | Qian | Hanqi | Qian
Melody A | Little Star | 10 | 10 | 2 | 2
Melody B | Happy birthday | 10 | 10 | 2 | 2
Melody C | Brother John | 10 | 10 | 2 | 2

## Slide 3
Feature Extraction
Read melody files
  Read files to get wav‘s sampling rate and signal data.
Get music feature
  Get pitch frequency, intensity and correlation of each melody.
Extract feature
  Eliminate noise components.
  Generate features based on semitones.

## Slide 4
Feature Extraction
Comparison of the features of three melodies

## Slide 5
HMM System Design
Training Set
Feature Extractor
HMM Training
Testing Set
Performance evaluation
HMM Model
Training Set
Feature
Testing Set
Feature

## Slide 6
HMM implementation
Design
  HMM parameter set .
Training
  Baum-Welch algorithm per song.
Prediction
  Forward algorithm
  a. Calculate per class given the obs sequence extracted from the test sample.
  b. Select the maximum probability.

## Slide 7
Trained Matrix
0.1885425 | 0.16211513 | 0.32020771 | 0.32913467
0.2688196 | 0.18329328 | 0.224296 | 0.32359112
0.20451465 | 0.33292653 | 0.27438849 | 0.18817034
0.30051905 | 0.27732585 | 0.20020113 | 0.22195397
0.30827782 | 0.23850963 | 0.20038111 | 0.25283144
q:
A:
mean | covariance
1.324885 | 2.33090732
1.32566065 | 2.33272433
1.32138294 | 2.32315641
1.3216786 | 2.32378083
1.324885 | 2.33090732
1.32566065 | 2.33272433
1.32138294 | 2.32315641
1.3216786 | 2.32378083
B:

## Slide 8
Result
 | Melody1 | Melody2 | Melody3
Test sample 1 | √ | ×(Misjudged as 3) | √
Test sample 2 | ×(Misjudged as 3) | ×(Misjudged as 3) | √
 | Melody1 | Melody2 | Melody3
Test sample 1 | √ | ×(Misjudged as 1) | ×(Misjudged as 1)
Test sample 2 | √ | ×(Misjudged as 1) | ×(Misjudged as 1)
10 training samples and 2 test samples per melody from Hanqi
10 training samples and 2 test samples per melody from Qian

## Slide 9
Result
 | Melody1 | Melody2 | Melody3
Test sample 1 | √ | ×(Misjudged as 3) | √
Test sample 2 | √ | ×(Misjudged as 3) | √
Test sample 3 | √ | ×(Misjudged as 3) | √
Test sample 4 | √ | ×(Misjudged as 3) | √
20 training samples and 4 test samples per melody from two persons

## Slide 10
Result and Problems
Correctness rate:
  50% (10 training samples and 2 test samples per melody from Hanqi)
  33.3% (10 training samples and 2 test samples per melody from Qian)
  66.6% (20 training samples and 4 test samples per melody from two persons)
Problems:
  Insufficient number of samples in the training set.
  The extracted features are not sufficient to distinguish the second song from
  the other two.
  Poor quality of HMM model.

## Slide 11
Conclusion and improvements
Conclusion:
  A pattern recognition system capable of distinguishing between a few brief
  snippets of hummed melodies. (66% correct rate)
Improvements:
  Increase dataset of melody B to get a higher accuracy.
  Increase the number and diversity of samples.
  Better feature extractor.
  Better HMM model.

## Slide 12
Thank you for your listening!
Hanqi Yang, hanqi@kth.se
Qian Zhou, qianzho@kth.se